Max. Source file length: ~2Gb
Max. database line number: ? 32000

1. CSV content:

1) Encoding – according to "CodePage" setting in the EscPosParser2.exe.config file (default "866")
2) Column divider - according to "CSVdelimiter" setting in the EscPosParser2.exe.config file (default ";")

2. Command data base columns:
1) Command (HEX) – command string [HEX string]
2) Command parameter size (DEC) – length of the parameter [byte]
3) Command parameter type – parameter type. Defines how to show/decode data.
4) Command parameter value (dec) – predefined parameter values if any.
5) Command description – description of command, parameter or predefined parameter
6) Reply parameter size (DEC) – length of the parameter [byte]
7) Reply parameter type – parameter type. Defines how to show/decode data.
8) Reply parameter value (dec) – predefined parameter values if any.
9) Reply description – description of command, parameter or predefined parameter
10) Comments – always ignored. Needed only for correct CSV handling.
All other columns ignored.

3. Possible parameter types:
1) string – displayed with “” if printable.
2) number – int number displayed.
3) money - numerical value displayed wit 2 chars after dot.
4) quantity - numerical value displayed wit 3 chars after dot.
5) error# - Length: until byte shown in predefined value;
6) data - Length: until byte shown in predefined value; String length displayed.
7) bitfield - Length: until byte shown in predefined value; A numerical value displayed.
8) password – operator number and password. Dispalyed as nn/pppp.
9) prefdata – prefixed data. 2 bytes at the beginning - length of data. Dispalyed as [xx]???.
10) tlvdata – fiscal data structure. 2 bytes – type, 2 bytes – length, data. Dispalyed as [tt]	[nn]???.

6. Command data base structure:
Each command or parameter must have it’s 1st line clear until “Description”.
Each parameter may have several predefined values to define proper description.	Description for predefined value is added to description of the parameter in the program GUI.
Each parameter must be followed by a parameter type definition.
“bitfield” parameter is followed by 8 lines describing each bit
Parameter size can be a number or "?" - then it's size assumed as "till the end of the frame" minus all following parameter sizes.